Wood Heights Fire Protection District

Ordinance No: 20100421b

An Ordinance requiring builders to install fire hydrants for fire suppression

in residential developments.

Be it ordered by the Wood Heights Fire Protection District Board members of Wood Heights, Missouri as follows:

- Builders will be required to install proper water line size of 6” and above to supply water to newly developed housing additions (as per planning and zoning specs of a residential development) with fire hydrants spaced at 800’ apart.

- Builders will be required to install all hydrants with 2-2.5” ports and 1-4.5” port using National Fire Threads (NST).

- 4.5” port will need to face main roadway and not face any other direction without the written consent of the Wood Heights Fire Protection District Fire Chief or board of directors.

- All Hydrants will be required to have a shut off within 3’ of the fire hydrant in case of repairs needed by the Water Dept.

- Shut off will need to be 2” square key type shut off and capped at final grade with a metal top hat style cap with a lid that shows “water”.

- If water main that is currently in place that is less than 6” in size the builder may apply for a variance from this ordinance and be approved by the Wood Heights Fire Protection District board of directors or be required to upgrade water main to comply with ordinance for fire protection.

ADOPTED AND APPROVED by the Wood Heights Fire Protection District board members of Wood Heights, Missouri on this 21st day of April, 2010

Approved

________________________

Ron Server-Board President

________________________

Eric White-Board Member

Attest

_________________________

Diane Teegarden-Secretary

_________________________

Lee O’Dell-Fire Chief